EQE- and JV-Analysis
of Tandem Solar Cells

---
Part 1: EQE-Analysis
- Task: Match two solar cells for use in a tandem solar cell
  - force same current by adjusting the thickness
- Given data:
  - EQE-Spectra of the top cell, the bottom cell and the bottom cell if covered by the top cell
  - Standard solar spectrum

---
Given Data
Top Cell: P3HT:PCBM
Bottom Cell: KP115:IDTBR

---
Step 1: Solar Spectrum to Current Spectrum

---
Step 2: EQE

---
Step 3: Scale Thickness Appropriately
\times 0.42

---
Step 3: Scale Current Appropriately

---
Part 2: JV-Analysis
- Task: Apply the correction factor to JV-Curves, discuss the effect on VOC, JSC, FF
- Given data:
  - JV-Curves of the uncorrected cells

---
Given Data

---
Step 1: Adjust JV-Curves

---
Step 2: Combine JV-Curves

---
Step 3: Calculate Peak Power

---
Results
	Initial Cells	Adjusted Cell
FF	0.51	0.51
VOC [V]	1.43	1.47
JSC [mA/cm²]	2.44	4.74
Peak Power [mW/cm²]	1.79	3.58

---
Step 1: Solar Spectrum to Current Spectrum
Power(\lambda) \rightarrow N(\lambda) = \frac{Power(\lambda)}{E_p_h(\lambda)}
N(\lambda) \rightarrow j(\lambda) = q \cdot N(\lambda)